## Slide 1: Existing Generating Resources – Inputs to the Models
RAAC/SAAC/GRAC
May 6, 2020 - Gillian Charles

## Slide 2: Existing System
Building resource blocks and translating into model inputs

## Slide 3: April 23 SAAC/RAAC/GRAC
Discussed existing system resources - what’s in, what’s out, and how to count them

## Slide 4: Project Database & Components
Project/Unit-level data
Resource fuel
Technology type
Nameplate capacity
Operating status
Location
Ownership/electrical load
Historical energy
… and many more!
Assumptions
Heat rate
Seasonal outages
… and many more!

## Slide 5: Existing System – Aggregate units
Aggregate unit-level data and sort into resource blocks
  Some resources have multiple blocks (ex. A)
  Some resources are aggregated into one block (ex. B)
Chart: Existing System Resources - Nameplate Capacity ~ 63,000 MW
| Hydro | Wind | Solar | Nuclear | Natural Gas | Coal | Biomass | Geothermal | Petroleum
 | 34276 | 10858.3 | 1109.3 | 1200 | 9631.2 | 4953.7 | 798.4 | 68.5 | 142.6
Gas West 1
Gas West 2
Gas West 3
Gas East 1
Gas East 2
Gas East 3
Chart: Existing System Resources - Nameplate Capacity ~ 63,000 MW
| Hydro | Wind | Solar | Nuclear | Natural Gas | Coal | Biomass | Geothermal | Petroleum
 | 34276 | 10858.3 | 1109.3 | 1200 | 9631.2 | 4953.7 | 798.4 | 68.5 | 142.6
Other Must Run
Example B: Biomass, Geothermal, Petroleum
Example A: natural gas

## Slide 6: Developing Resource Blocks
Each resource block has attributes that have been aggregated from unit-level data
  Nameplate capacity (MW), average heat rate, average fixed O&M, average variable O&M, average forced outage rate, etc.
The model dispatches resources by block to meet load; dispatch considers the heat rate and VOM, along with fuel and electricity prices

## Slide 7: Draft 2021 Plan – Generating Resource Blocks
Gas West 1
Gas West 2
Gas West 3
Gas East 1
Gas East 2
Gas East 3
Wind
Solar
Where is hydro? Hydro generation info is provided by BPA thru PNCA; includes operating constraints and variations due to water conditions
CGS
Other Must Run
Colstrip 4
Colstrip 3
Announced Retirements
Other Coal
Notes: PNCA -

## Slide 8: Coal – The Ins and Outs
What’s IN:
Jim Bridger 1 (ret EOY 2023)
Centralia 2 (ret EOY 2025)
North Valmy 2 (ret EOY 2025)
Jim Bridger 2 (ret EOY 2028)
Colstrip 3
Colstrip 4
Jim Bridger 3, 4
Montana One (Colstrip Energy)
Amalgamated Sugar
What’s OUT:
Boardman (ret EOY 2020)
Centralia 1 (ret EOY 2020)
Colstrip 1, 2 (ret EOY 2019)
Hardin (OOR; ???)
North Valmy 1 (ret EOY 2021; IPC ended “participation” in EOY 2019)
EOY = end of year; OOR = out of region
Colstrip 4
Colstrip 3
Announced Retirements
Other Coal
Review

## Slide 9: RPM Inputs & Formulas
Parameter | Description
Resource size (MW) | Sum of installed nameplate capacity of units in resource block
Fixed O&M ($-kw/year) - Includes operating and maintenance, labor and materials, and administrative overhead (routine maintenance, and major maintenance and capital replacement are assumed to be included) | Weighted-average FOM of units in resource block; based on average historical data (5 years) or best available info
Variable O&M ($/MWh) - Includes all costs that are a function of the amount of power produced (consumables such as water, chemicals, lubricants, and catalysts, and waste disposal) | Weighted-average VOM of units in resource block; based on average historical data (5 years) or best available info
Forced outage rate (%) - expected number of hours a resource is forced out of service (i.e. unplanned outage) divided by the total number of hours in the year | Weighted-average FOR of units in resource block
Maintenance outage rate - expected number of hours a resource will be out of service during the year for planned maintenance divided by the total number of hours in the year | Seasonal weighted-average MOR of units in resource block
Heat rate (MMBtu/MWh) - amount of input (fuel) energy required by a power plant to produce one kilowatt-hour of electrical output | Weighted-average heat rate of units in resource group; Based on average of last five years, or best available information
Fraction dedicated to region – expectation that the region bears the fixed cost of the resource | Weighted-average RPM % rate-based to region of units in resource group
Capability available to region - amount resource can be dispatched to the region | Weighted-average RPM % capability to region of units in resource group

## Slide 10: Contributions to the Existing System
How do we determine which resources “count” towards the region, and at what amount?
e.g. IPP-owned resource, uncommitted load (market)
e.g. NorthWestern Energy owned/contracted resource
e.g. PacifiCorp OOR renewable resource
e.g. Resources that have been idled or mothballed
e.g. IPP resource w/ OOR long-term PPA
e.g. Joint ownership, multiple load shares
Percent Rate - Based to the Region – the expectation that the region bears the fixed cost of the resource
Percent Capability to the Region – amount resource can be dispatched to the region
Review

## Slide 11: What do the resource blocks look like as inputs in the model and how do they contribute to the system?

## Slide 12: Background

## Slide 13
Planned retirements based on agreements, announcements, IRPs; subject to change
Idaho Power intends to end its participation in North Valmy 1 in 2019
Uncertainty remains over timing of Jim Bridger 1,2 potential accelerated retirements
Hardin Generating Station was sold to an out-of-region cryptocurrency company; therefore no longer “counts” towards the region
Colstrip 3,4 should be considered very tentative
Updated Mar 2020
Data source: Council’s project database