## Slide 1: 2021 Adequacy Assessment Data Requirements Resource Adequacy Advisory Committee
Technical Committee Meeting
March 18, 2016

## Slide 2: Data Elements
Hydro
  Sustained Peak vs. Energy curves
  Balancing Reserves
Hourly loads
  Energy Efficiency
  Firm contracts
Generating resources
  Independent Power Producers
  Market Availability
  Wind
  Solar
Standby (emergency) resources
Transmission

## Slide 3: Hydro
Summary | Modified stream flows, rule curves, plant data, operating constraints
Lead | Pat Byrne (BPA)
Source | 2015 BPA HYDSIM data for 2021 OP year
File Name | Multiple files
Format | Text and binary
Status | Received data, processing it now
Location | Adequacy/2016 for 2021/Data/Hydro

## Slide 4: Hydro Peak vs. Energy Curves
Summary | Sustained peak as function of period energy 2, 4 and 10 hour sustained peak durations 5-point piecewise-linear function End points equal low and high values Mid-points are evenly spaced
Lead | Ben Kujala (Council)
Source | Trapezoidal model and PREP program
File Name | SustPeak.dat
Format | Text file
Status | 7th plan data, to be updated with new Hydro data and revised balancing reserve assumptions
Location | Adequacy/2016 for 2021/Data/Hydro

## Slide 5: Balancing Reserves
Summary | Regional balancing reserves held by hydro (incorporated into the SustPeak.dat file) BPA: 400/900 MW INC/DEC April-July 900/900 MW INC/DEC August-March Rest of region: 1,829/1,799 MW INC/DEC (max) Non-hydro: 958/1,264 MW INC/DEC (max)
Lead | John Ollis (Council)
Source | Trapezoidal model and PREP program
File Name | SustPeak.dat
Format | Text file
Status | 7th plan data, to be updated with new Hydro data and revised INC/DEC requirements
Location | Adequacy/2016 for 2021/Data/Hydro

## Slide 6: Hourly Loads STM
Summary | 8,760 hourly loads (rows) for 80 temp years (columns) No leap year data Does include projected EE savings New codes and standards are not accounted for East/West load split factors 0.39/0.61
Lead | Massoud Jourabchi (Council)
Source | Short-term load forecasting model
File Name | HourlyLoadsSTM.bin
Format | Binary file
Status | Yet to be converted into binary format
Location | Adequacy/2016 for 2021/Data/Loads

## Slide 7: Hourly Loads LTM
Summary | 8,760 hourly loads (rows) for 80 temp years (columns) No leap year data Does not include any projected EE savings New codes and standards are accounted for East/West load split factors 0.39/0.61 Loads stretched to user input quarterly peak/mean values
Lead | Massoud Jourabchi (Council)
Source | Long-term load forecasting model Load Stretching program
File Name | HourlyLoadsFE.bin
Format | Binary file
Status | Yet to be converted into binary format
Location | Adequacy/2016 for 2021/Data/Loads

## Slide 8: Energy Efficiency
Summary | Energy and peak savings incorporated into the Load file Quarterly peak and mean savings from RPM Oct-Mar peak savings = 1.9 times mean savings Apr-Sep peak savings = 1.2 times mean savings Hourly savings prorated by load stretching program
Lead | Charlie Grist (Council)
Source | Load Stretching Program or STM
File Name | HourlyLoadsFE_EE.bin HourlyLoadsSTM.bin includes EE projections
Format | Binary file
Status | 7th plan data, to be updated with new Hydro data
Location | Adequacy/2016 for 2021/Data/Loads

## Slide 9: Firm Contracts
Summary | Firm extra-regional imports and exports Includes the Canadian entitlement Monthly energy On-peak and off-peak contributions
Lead | Pat Byrne (BPA)
Source | 2015 BPA White Book
File Name | Contracts.dat
Format | Text file
Status | Received data, processing now
Location | Adequacy/2016 for 2021/Data/Loads

## Slide 10: Generating Resources
Summary | Capacity, heat rate, FOR, Maintenance schedule, etc. for thermal, Independent power producers, spot market imports (all hours), spot market purchase-ahead imports (off-peak hours for month, window, day), misc
Lead | Gillian Charles (Council)
Source | Council’s Generating Resources Database
File Name | Genres.dat
Format | Text file
Status | 7th plan data
Location | Adequacy/2016 for 2021/Data/Resources

## Slide 11: Independent Power Producers
Summary | Capacity, heat rate, FOR, Maintenance schedule, etc. for Independent power producers Full availability from Oct-Mar 1,000 MW max available from Apr-Sep
Lead | Gillian Charles (Council)
Source | Council’s Generating Resources Database
File Name | Genres.dat
Format | Text file
Status | 7th plan data Should be priced at market prices for proper dispatch
Location | Adequacy/2016 for 2021/Data/Resources

## Slide 12: Spot Market
Summary | Modeled as a CA resource Capacity, heat rate, FOR, Maintenance schedule, etc. 2,500 MW max in any hour Oct-Mar None available in Apr-Sep
Lead | Gillian Charles (Council)
Source | Energy GPS Report, RAAC
File Name | Genres.dat
Format | Text file
Status | 2015 Adequacy Assessment assumptions
Location | Adequacy/2016 for 2021/Data/Resources

## Slide 13: Purchase Ahead Market
Summary | Modeled as a CA resource Capacity, heat rate, FOR, Maintenance schedule, etc. 3,000 MW max any month during off-peak hours
Lead | Gillian Charles (Council)
Source | Energy GPS Report, RAAC
File Name | Genres.dat
Format | Text file
Status | 2015 Adequacy Assessment assumptions
Location | Adequacy/2016 for 2021/Data/Resources

## Slide 14: Wind
Summary | 8,760 hourly capacity factors (rows) for 77 temp (columns) 20 sets of 8,760 by 77 data Up to 3 sites
Lead | Ben Kujala (Council)
Source | BPA: temperature-correlated hourly capacity factors
File Name | BPAWind_01.bin to BPAWind_20.bin RegWind.bin, non-BPA regional wind CAWind.bin, wind dedicated to serve CA
Format | Binary files
Status | Currently only the BPA wind fleet data is available Waiting for other regional wind data Waiting for data for CA wind located in the region Waiting for code updates to handle 3 independent sites
Location | Adequacy/2016 for 2021/Data/Wind

## Slide 15: Solar
Summary | 8,760 hourly capacity factors (rows) for XX years (columns) Up to 3 sites
Lead | Steve Simmons (Council)
Source | S Idaho New: NREL data S Idaho Existing: Idaho Power Existing: Generating Resource Database
File Name | IdSolar.bin, IPCoSolar.bin, OtherSolar.bin Data for existing wind currently resides in Genres.dat and has fixed monthly and hourly generation
Format | Binary file, same format as wind data
Status | S Idaho New: 12 years of NREL data is available Existing solar comes from Resource Database S Idaho Existing: Waiting for Idaho Power data Waiting for code updates to handle 3 independent sites
Location | Adequacy/2016 for 2021/Data/Solar

## Slide 16: Standby Resources
Summary | Small dispatchable generation, new DR, Banks Lake pumped storage Implemented via post processor Monthly energy and capacity limits
Lead | Rob Diffely (BPA)
Source | Many
File Name | Standby.dat
Format | Text file
Status | Updated to 2016 data Waiting for code to implement seasonal use limits
Location | Adequacy/2016 for 2021/Data/Resources

## Slide 17: Transmission
Summary | Inter-nodal transmission capacity limits
Lead | Ben Kujala (Council)
Source | AURORA, other sources
File Name | Trans.dat
Format | Text file
Status | Using 2015 data Need to ensure consistency with other models Need to add uncertainty (e.g. FOR) for NW-SW interties Waiting to update east/west NOMOGRAM from BPA
Location | Adequacy/2016 for 2021/Data/Transmission