## Slide 1: 2021 Adequacy Assessment Reference Case and Scenarios Resource Adequacy Advisory Committee
Technical Committee Meeting
March 18, 2016

## Slide 2: Reference Case (Based on 7th Plan Assumptions)
Adjusted LTM loads with RPM expected EE and DR
Import availability
  Spot (2500 MW all hours winter, 0 summer)
  Purchase Ahead (3000 MW off-peak hours, all year)
IPP generation
  Full availability winter
  1000 MW summer
EE quarterly mean and peak from RPM
Regional wind modeled as BPA wind
Regional solar has fixed generation pattern

## Slide 3: Suggested Scenarios
Reference Studies (using LTM loads)
  Reference Case (med load, 2500 MW import)
  Load Ranges (low, med-low, med, med-high, high)
  Import Ranges (0, 1700, 2500, 3400,4500)
Sensitivity Studies
Reference Case using STM loads
Fuel Limitation
  Remove Gray’s Harbor
  Remove it at low temperature threshold (code change)
Use STM conservation shape (if different)
No new DR case

## Slide 4: Number of Studies
Reference Case (LTM) 1
Load Ranges X Import Ranges 24
Reference Case (STM) 1
Fuel Limitation 2
No new DR 1
Conservation shapes 1
Total 30

## Slide 5: Not Modeled for 2021
Import uncertainty
  Uncertainty in availability of the intertie
  Uncertainty in availability of CA resources
Market friction
  Is adding uncertainty to the imports sufficient
  Should imports be a function of temperature
Economic load uncertainty
  Instead of high and low load scenarios
  Built in as a random variable