## Slide 1: Working Towards Better Savings Estimates for HVAC and Weatherization Measures
Regional Technical Forum
September 16, 2014

## Slide 2: Overview
Brief description of SEEM
Role of the recent calibration
Our path and the decisions we made
Moving forward

## Slide 3: What is SEEM?
SEEM is a simulation model used to give us a sense of what is going on in a building based off the physics of heat transfer and other engineering basics.

## Slide 4: Value of Calibration
In the real world houses and people are different
The calibration helps us use the model to more accurately reflect what might happen on average with real houses and real people

## Slide 5: What the Model Gets Wrong
Temperature of House:
  This can be difficult to get in a reliable way, but it is a critical input
Internal gains:
  Lighting, warm bodies, other equipment, etc.
Model parameters
Location/weather
Floor area
Foundation
Heating equipment
Duct tightness
Attic R
Wall R
⋮
Thermostat setting
Internal gains
Behavior
⋮
Some things pretty well-known
Others not so much

## Slide 6: This Isn’t our First Calibration
Date | RTF Decision Summary | Housing Type | T-stat Results | Data Sources Used in Calibration
Nov-2009 | SEEM 92 model is calibrated. | Single Family | HP & Gas FAF 70°F Day ; 64°F Night Electric FAF and Zonal 66°F Day & Night | 1. Res New Const. Billing Analysis (RLW 2007) 2. SGC Metered Data 3. NEEA Heat Pump Study (2005) Note: Very limited representation of Zones 2 & 3
Apr-2011 | SEEM 93 model is calibrated. (implicit decision) | Single Family with GSHP | 70°F Day ; 64°F Night | 1. Missoula GSHP Study (1996)
Dec-2011 | Use updated SEEM94 model | Single Family, Manufactured Home | n/a | Ecotope updated SEEM code to model the physics of the house infiltration, rather than rely on a constant stipulated infiltration rate input in previous versions of SEEM.
Dec-2011 | SEEM 94 model is calibrated | Manufactured Home | 69.4°F Day 61.6°F Night | 1. NEEM 2006 2. NEEA Heat Pump Study (2005) 3. MAP 1995 4. RCDP (manufactured homes)
Sep-2012 | SEEM 94 model is calibrated | Multifamily | Walk-up and Corridor 68°F Day& Night Townhouses 66°F Day & Night | 1. Multifamily MCS (SBW 1994) 2. MF Wx Impact Evaluation for PSE (SBW 2011) 3. New Multifamly Building Analysis (Ecotope 2009) 4. ARRA Verification for King County (Ecotope 2010)

## Slide 7: Why Do Another SEEM Calibration?
We have a new, robust data set in the Residential Building Stock Assessment (RBSA)
Survey of 1404 homes in WA, OR, ID, MT
Physical building characteristics
Site-level billing data summaries
Occupant interview data

## Slide 8: Our Journey
Start: Old SEEM
Phase I:
2012 – May 2013 (SF)
Dec 2013 (SF)
Mar 2014 (SF, NC)
Jun 2014 (MH)
Phase II:
May 2013 – Sep 2013 (SF)
Jun 2014 (SF and MH)
Are we there yet?
Option 3:
Oct 2013 and Jun 2014

## Slide 9: Overview of our Journey
Basic idea: Based on a sample of audited homes, identify and estimate systematic differences between SEEM-based and bill-based heating energy estimates.
The RTF Process:
Phase I. Differences in total heating energy
Phase II. Differences in electric heating energy (our interest is the impact to the grid)
Additional RTF Analysis Option 3. Interactive effects of measures

## Slide 10: Where we Started
New version of SEEM  improved engineering model
  Air infiltration
  Floor and ducts interaction
Previous calibration did not focus on the grid impact
Used last measure in (LMI) and assumed installation of all measures

## Slide 11: Phase I
Address Total Heating Energy
2012 – June 2014
Focus on houses where we have a good estimate of heating use (“clean heating signature”)
Compare data from houses in the real world to similar houses coming out of SEEM
The difference between these can inform other results for which we don’t have billing data
Phase I-calibrated SEEM estimates should align simulated results with billing data (on average) for “clean” homes

## Slide 12: Calibration Results
Increase SEEM for efficient homes and decrease for inefficient homes
Chart: 
| 7.5000000000000094E-2 | 8.000000000000014E-2 | 8.5000000000000048E-2 | 9.0000000000000066E-2 | 9.5000000000000154E-2 | 0.1 | 0.10500000000000002 | 0.1100000000000001 | 0.11500000000000012 | 0.12000000000000002 | 0.125 | 0.13 | 0.13500000000000001 | 0.14000000000000001 | 0.14500000000000021 | 0.15000000000000024 | 0.15500000000000028 | 0.16000000000000023 | 0.16500000000000026 | 0.17 | 0.17500000000000004 | 0.18000000000000024 | 0.18500000000000025 | 0.19000000000000022 | 0.19500000000000026 | 0.2 | 0.20500000000000004 | 0.21000000000000021 | 0.21500000000000025 | 0.22000000000000022 | 0.22500000000000026 | 0.23 | 0.23500000000000001 | 0.24000000000000021 | 0.24500000000000025 | 0.25
Z1 - Elec.Res. | 1.0392 | 1.0213 | 1.0034 | 0.98549 | 0.9676 | 0.94971 | 0.93181 | 0.91392 | 0.89603 | 0.87814 | 0.86025 | 0.84235 | 0.82446 | 0.80657 | 0.78868 | 0.77079 | 0.7529 | 0.735 | 0.71711 | 0.69922 | 0.68133 | 0.66344 | 0.64554 | 0.62765 | 0.60976 | 0.59187 | 0.59187 | 0.59187 | 0.59187 | 0.59187 | 0.59187 | 0.59187 | 0.59187 | 0.59187 | 0.59187 | 0.59187
Z1 - Gas/HP | 1.3304 | 1.3077 | 1.2851 | 1.2625 | 1.2398 | 1.2172 | 1.1945 | 1.1719 | 1.1493 | 1.1266 | 1.104 | 1.0813 | 1.0587 | 1.0361 | 1.0134 | 0.99077 | 0.96813 | 0.94549 | 0.92285 | 0.90021 | 0.87757 | 0.85492 | 0.83228 | 0.80964 | 0.787 | 0.76436 | 0.76436 | 0.76436 | 0.76436 | 0.76436 | 0.76436 | 0.76436 | 0.76436 | 0.76436 | 0.76436 | 0.76436
Phase I: Adjustment Factor vs Efficiency of Envelope
Uo
More Efficient
Less Efficient

## Slide 13: Phase II
Impact on the Grid: Adjustment for Electric Heating Energy
May 2013 – June 2013
To focus on savings on the grid, we need to adjust for savings related to off-grid heat (ex: wood or gas)
    Off-grid fuels okay, but must have permanent electric heat too
Run another regression analysis to estimate how high gas or wood heat affects electric heating energy
Calibration Results: Expect to see about 83% of Phase-I kWh on the grid.

## Slide 14: Update on our Journey
Start: Old SEEM
Phase I:
2012 – May 2013 (SF)
Dec 2013 (SF)
Mar 2014 (SF, NC)
Jun 2014 (MH)
Phase II:
May 2013 – Sep 2013 (SF)
Jun 2014 (SF and MH)
Are we there yet?
Option 3:
Oct 2013 and Jun 2014

## Slide 15: Option 3
Addressing Measure Interactions
October 2013 – June 2014
Analyzed several different approaches for addressing the interaction between measures and ended on the third option presented (hence “Option 3”)
A way to distribute savings amongst interactive measures without knowing what is already in the house or what might be installed down the road
Program easing strategy

## Slide 16: Where are we Now?
Start: Old SEEM
Phase I:
2012 – May 2013 (SF)
Dec 2013 (SF)
Mar 2014 (SF, NC)
Jun 2014 (MH)
Phase II:
May 2013 – Sep 2013 (SF)
Jun 2014 (SF and MH)
Option 3:
Oct 2013 and Jun 2014
Are we there yet?

## Slide 17: Where are we Now?
Implementing these RTF decisions (Phase I, Phase II, and Option 3) for single family weatherization and HVAC measures to come up with new savings
RTF asked for more analysis in a few specific areas before making a decision on the proposed measures  Results presented at Sept Meeting

## Slide 18: Outcomes of September Meeting
RTF adopted the updated savings and costs for single family weatherization UES measures
Asked for Contract Analysts to add measure identifiers to heat pump conversion measures
  Different measures depending on what level of insulation is already in the house
Will come back to RTF with the these measure identifiers for consideration of HVAC UES measures

## Slide 19: Our Next Journey
The impact of these changes on programs is significant
Staff are here to help answer questions that come our way
Thinking through a communications plan to inform implementers
Questions for the PAC
Is there more we (Jenn and Charlie) should be doing?
What is the role of the PAC in helping to convey the message